## Slide 2: Lilypad Arduino Workshop
By Venkat Venkataraju and Jeremiah Wuenschel

## Slide 3: Blinking Lights
Controlling LED lights

## Slide 4: A Touch Of Color
Controlling the color of the multi color LED

## Slide 5: Pushing Buttons
Responding to a push button

## Slide 6: Why Debounce?
Switches are not perfect
The contact connection and disconnect are not clean
Produces a period of instability in the signal

## Slide 7: Debouncing an Input

## Slide 8: Solution - from Adafruit
void loop() {
int switchstate;
reading = digitalRead(inPin);
if (reading != previous) {
time = millis();
}
if ((millis() - time) > debounce) {
switchstate = reading;
if (switchstate == HIGH)
LEDstate = LOW;
else
LEDstate = HIGH;
}
digitalWrite(outPin, LEDstate);
previous = reading;
}

## Slide 9: Pull-Up and Pull-Down Resistor

## Slide 10: Fading Lights
Changing the brightness of the LED

## Slide 11: Pulse-width Modulation
Microcontrollers can only output 0 or 1
By toggling the pin “on” 50% of the time, we can reduce the total power output to 50%
By varying the % of time the pin is on, we can simulate analog output
For a cleaner signal, the PWM output can be passed thru a RC filter circuit

## Slide 12: Pulse-width Modulation

## Slide 13: Making Noise
Generating Sound

## Slide 14: Sensing Light
Responding to ambient light

## Slide 15: More…
Slide Switch (Pin D2)
Temperature sensor (Pin A1)
Vibe Board (Pin 3)

## Slide 16: Resources
Arduino Documentation
http://arduino.cc/en/Reference/HomePage
Lilypad Arduino Reference
http://lilypadarduino.org/
Lilypad ProtoSnap Schematics
http://dlnmh9ip6v2uc.cloudfront.net/datasheets/E-Textiles/Lilypad/LilyPad-Dev-v34b.pdf
Debouncing
http://arduino.cc/en/Tutorial/Debounce
http://www.engscope.com/pic-example-codes/basic-io-button-debounce/
http://learn.adafruit.com/tilt-sensor/using-a-tilt-sensor
Pulse-width modulation
http://arduino.cc/en/Tutorial/PWM
http://www.protostack.com/blog/2011/06/atmega168a-pulse-width-modulation-pwm/
Pull-ups and pull-downs
https://learn.sparkfun.com/tutorials/pull-up-resistors